## Slide 1: SWE 425: Telecommunication Engineering
Md. Habibur Rahman
Lecturer, Department of Software Engineering

## Slide 2: Transmission Control Protocol (TCP)
The Transmission Control Protocol (TCP) is one of the main protocols of the Internet protocol suite.
It originated in the initial network implementation in which it complemented the Internet Protocol (IP). Therefore, the entire suite is commonly referred to as TCP/IP.
TCP provides reliable, ordered, and error-checked delivery of a stream of octets between applications running on hosts communicating by an IP network.
Major Internet applications such as the World Wide Web, email, remote administration, and file transfer rely on TCP.

## Slide 3: Characteristics of TCP Protocol
Connection-oriented, point-to-point protocol:
  Connection establishment and teardown phases
  ‘Phone-like’ circuit abstraction (application-layer view)
  One sender, one receiver
  Called a “reliable byte stream” protocol
  General purpose (for any network environment)
Originally optimized for certain kinds of transfer:
  Telnet (interactive remote login)
  FTP (long, slow transfers)
  Web is like neither of these!

## Slide 4
Provides a reliable, in-order, byte stream abstraction:
  Recover lost packets and detect/drop duplicates
  Detect and drop corrupted packets
  Preserve order in byte stream, no “message boundaries”
  Full-duplex: bi-directional data flow in same connection
Flow and congestion control:
  Flow control: sender will not overwhelm receiver
  Congestion control: sender will not overwhelm the network
  Sliding window flow control
  Send and receive buffers
  Congestion control done via adaptive flow control window size
socket
layer
TCP
send buffer
application
writes data
TCP
receive buffer
socket
layer
application
reads data
data segment
ACK segment
Characteristics of TCP Protocol

## Slide 5: Challenges of Reliable Data Transfer
Over a perfectly reliable channel
  All of the data arrives in order, just as it was sent
  Simple: sender sends data, and receiver receives data
Over a channel with bit errors
  All of the data arrives in order, but some bits corrupted
  Receiver detects errors and says “please repeat that”
  Sender retransmits the data that were corrupted
Over a lossy channel with bit errors
  Some data are missing, and some bits are corrupted
  Receiver detects errors but cannot always detect loss
  Sender must wait for acknowledgment (“ACK” or “OK”)
  … and retransmit data after some time if no ACK arrives

## Slide 6: ADVANTAGES OF TCP
TCP always guarantees three things - your data reaches its destination, it reaches there in time and it reaches there without duplication.
In TCP, since all the work is done by the operating system, so you just need to sit back and watch the show. Even the debugging is taken care of by your OS.
It automatically breaks up data into packets for you.
The operating system does all the work. you just sit back and watch the show. no need to have the same bugs in your code that everyone else did on their first try; it's all been figured out for you.
Routers may notice TCP packets and treat them specially. they can buffer and retransmit them.
TCP has good relative throughput on a modem or a LAN.

## Slide 7: DISADVANTAGES OF TCP
It is slower in functioning than UDP.
Since, all the work is being done by your OS, so if there are bugs in your OS, then you will face many problems like problems in surfing and downloading contents from the net.
TCP cannot be used for broadcast and multicast connections
TCP bandwidth, high latency link, such as a satellite connection or an overfull t1.
TCP cannot conclude a transmission without all data in motion being explicitly acknowledged.

## Slide 8: TCP Segment Structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
Receive window
Urg data pnter
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
# bytes
rcvr willing
to accept
counting
by bytes
of data
(not segments!)
Internet
checksum
(as in UDP)

## Slide 9: TCP Segment Structure

## Slide 10: Example 1

## Slide 11: Example 1: Solution

## Slide 12: Example 1: Solution (Cont.)

## Slide 13: Connection Establishment (cont)
Host A
Host B
SYN, Seq=42
SYN+ACK, Seq=79, ACK=43
ACK, Seq=43, ACK=80
time
Three-way handshake
Three way handshake:
Step 1: client host sends TCP SYN segment to server
  specifies a random initial seq #
  no data
Step 2: server host receives SYN, replies with SYNACK segment
  server allocates buffers
  specifies server initial seq. #
Step 3: client receives SYNACK, replies with ACK segment, which may contain data
time
Connection
request
host ACKs and selects
its own initial seq #
host ACKs

## Slide 14: Connection Establishment (cont)
Host A
Host B
SYN, Seq=42
SYN+ACK, Seq=79, ACK=43
ACK, Seq=43, ACK=80
time
Three-way handshake
time
Connection
request
host ACKs and selects
its own initial seq #
host ACKs
Seq. #’s:
  byte stream “number” of first byte in segment’s data
ACKs:
  seq # of next byte expected from other side
  cumulative ACK

## Slide 15: TCP Connection Termination
Closing a connection:
client closes socket: clientSocket.close();
Step 1: client end system sends TCP FIN control segment to server
Step 2: server receives FIN, replies with ACK. Server might send some buffered but not sent data before closing the connection. Server then sends FIN and moves to Closing state.
client
FIN
server
ACK
ACK
FIN
close
Data
write
closed
timed wait
close
ACK
DATA

## Slide 16: TCP Connection Termination
Step 3: client receives FIN, replies with ACK.
  Enters “timed wait” - will respond with ACK to received FINs
Step 4: server, receives ACK. Connection closed.
Why wait before closing the connection?
  If the connection were allowed to move to CLOSED state, then another pair of application processes might come along and open the same connection (use the same port #s) and a delayed FIN from an earlier incarnation would terminate the connection.
client
FIN
server
ACK
ACK
FIN
closing
closing
closed
timed wait
closed

## Slide 17: TCP Retransmissions

## Slide 18: Automatic Repeat reQuest (ARQ)
Time
Packet
ACK
Timeout
Automatic Repeat Request
  Receiver sends acknowledgment (ACK) when it receives packet
  Sender waits for ACK and timeouts if it does not arrive within some time period
Sender
Receiver

## Slide 19: Reasons for Retransmission
Packet
ACK
Timeout
Packet
ACK
Timeout
Packet
Timeout
Packet
ACK
Timeout
Packet
ACK
Timeout
Packet
ACK
Timeout
ACK lost
DUPLICATE PACKET
Packet lost
Early timeout
DUPLICATE PACKETS
Notes: Application may get duplicates in the case of early timeouts

## Slide 20: TCP vs UDP
 | TCP | UDP
Acronym for | Transmission Control Protocol | User Datagram Protocol or Universal Datagram Protocol
Connection | TCP is a connection-oriented protocol. | UDP is a connectionless protocol.
Function | As a message makes its way across the internet from one computer to another. This is connection based. | UDP is also a protocol used in message transport or transfer. This is not connection based which means that one program can send a load of packets to another and that would be the end of the relationship.
Usage | TCP is suited for applications that require high reliability, and transmission time is relatively less critical. | UDP is suitable for applications that need fast, efficient transmission, such as games. UDP's stateless nature is also useful for servers that answer small queries from huge numbers of clients.
Ordering of data packets | TCP rearranges data packets in the order specified. | UDP has no inherent order as all packets are independent of each other. If ordering is required, it has to be managed by the application layer.
Speed of transfer | The speed for TCP is slower than UDP. | UDP is faster because error recovery is not attempted. It is a "best effort" protocol.
Reliability | There is absolute guarantee that the data transferred remains intact and arrives in the same order in which it was sent. | There is no guarantee that the messages or packets sent would reach at all.
Header Size | TCP header size is 20 bytes | UDP Header size is 8 bytes.

## Slide 21: TCP vs UDP (continued…)
 | TCP | UDP
Streaming of data | Data is read as a byte stream, no distinguishing indications are transmitted to signal message (segment) boundaries. | Packets are sent individually and are checked for integrity only if they arrive. Packets have definite boundaries which are honored upon receipt, meaning a read operation at the receiver socket will yield an entire message as it was originally sent.
Weight | TCP is heavy-weight. TCP requires three packets to set up a socket connection, before any user data can be sent. TCP handles reliability and congestion control. | UDP is lightweight. There is no ordering of messages, no tracking connections, etc. It is a small transport layer designed on top of IP.
Data Flow Control | TCP does Flow Control. TCP requires three packets to set up a socket connection, before any user data can be sent. | UDP does not have an option for flow control
Error Checking | TCP does error checking and error recovery. Erroneous packets are retransmitted from the source to the destination. | UDP does error checking but simply discards erroneous packets. Error recovery is not attempted.
Acknowledgement | Acknowledgement segments | No Acknowledgment
Handshake | SYN, SYN-ACK, ACK | No handshake (connectionless protocol)

## Slide 22
Thank You !!!
Any Questions ???