## Slide 1: SWE 425: Telecommunication Engineering
Md. Habibur Rahman
Lecturer, Department of Software Engineering

## Slide 2: Cellular Concept

## Slide 3
Interference and System Capacity
Sources of interference
  another mobile in the same cell
  a call in progress in the neighboring cell
  other base stations operating in the same frequency band
  Non cellular system leaks energy into the cellular frequency band
Two major cellular interference
  co-channel interference
  adjacent channel interference

## Slide 4
Co-channel Interference and System Capacity
Frequency reuse - there are several cells that use the same set of frequencies
  co-channel cells
  co-channel interference
To reduce co-channel interference, co-channel cell must be separated by a minimum distance.
When the size of the cell is approximately the same
  co-channel interference is independent of the transmitted power
  co-channel interference is a function of
    R: Radius of the cell
    D: distance to the center of the nearest co-channel cell
Increasing the ratio Q=D/R, the interference is reduced.
Q is called the co-channel reuse ratio

## Slide 5
For a hexagonal geometry
A small value of Q provides large capacity
A large value of Q improves the transmission quality - smaller level of co-channel interference
A tradeoff must be made between these two objectives

## Slide 6
Consider only the first layer of interfering cells
n = path loss exponent
S/I = Signal to Interference Ratio
Example: AMPS requires that SIR be greater than 18dB
  N should be at least 6.49 for n=4.
  Minimum cluster size is 7
Notes: Path Loss exponent:
In the study of wireless communications, path loss can be represented by the path loss exponent, whose value is normally in the range of 2 to 4 (where 2 is for propagation in free space, 4 is for relatively lossy environments and for the case of full specular reflection from the earth surface—the so-called Flat Earth model). In some environments, such as buildings, stadiums and other indoor environments, the path loss exponent can reach values in the range of 4 to 6. On the other hand, a tunnel may act as a waveguide, resulting in a path loss exponent less than 2.
Path loss is usually expressed in dB. In its simplest form, the path loss can be calculated using the formula
L = 10n log 10 (d) + C
Where L is the path loss in decibels, n is the path loss exponent, d is the distance between the transmitter and the receiver, usually measured in meters, and C is a constant which accounts for system losses.

## Slide 7: Problem:

## Slide 8: Solution:

## Slide 9
Adjacent Channel Interference
Adjacent channel interference: interference from adjacent in frequency to the desired signal.
  Imperfect receiver filters allow nearby frequencies to leak into the passband
  Performance degrade seriously due to near-far effect.

## Slide 10: Adjacent Channel Interference
Adjacent channel interference can be minimized through careful filtering and channel assignment.
Since each cell is given only a fraction of all available channels, a cell need not be assigned channels which are all adjacent in frequency.
By keeping the frequency separation between each channel in a given cell as large as possible, the adjacent channel interference may be reduced considerably.

## Slide 11: Trunking:
The concept of trunking allows a large number of users to share the relatively small number of channels in a cell by providing access to each user, on demand, from a pool of available channels.

## Slide 12: Grade of Service (GOS):
The Grade of Service (GOS) is a measure of the ability of a user to access a trunked system during the busiest hour.
It is a benchmark used to define the desired performance of a particular trunked system.
Grade of Service (GOS) is the likelihood that a call is blocked or delayed.

## Slide 13
Trunking and Grade of Service:
Erlangs:
One Erlangs represents the amount of traffic density carried by a channel that is completely occupied.
  Ex: A radio channel that is occupied for 30 minutes during an hour carries 0.5 Erlangs of traffic.
Each user generates a traffic intensity of Erlangs given by
H: average duration of a call.
: average number of call requests per unit time
For a system containing U users and an unspecified number of channels, the total offered traffic intensity A, is given by

## Slide 14: Erlang B Chart:

## Slide 15: Problem:

## Slide 16: Solution:

## Slide 17
Improving Capacity in Cellular Systems
Methods for improving capacity in cellular systems
  Cell Splitting: subdividing a congested cell into smaller cells.
  Sectoring: directional antennas to control the interference and frequency reuse.
  Coverage zone : Distributing the coverage of a cell and extends the cell boundary to hard-to-reach place.

## Slide 18
Cell Splitting
Split congested cell into smaller cells.
  Preserve frequency reuse plan.
  Reduce transmission power.
microcell
Reduce R to R/2

## Slide 19
Sectoring
Decrease the co-channel interference and keep the cell radius R unchanged
  Replacing single omni-directional antenna by several directional antennas
  Radiating within a specified sector

## Slide 20
Interference Reduction
position of the mobile
interference cells

## Slide 21
Microcell Zone Concept
Antennas are placed at the outer edges of the cell
Any channel may be assigned to any zone by the base station
Mobile is served by the zone with the strongest signal.
Handoff within a cell
  No channel re-assignment
  Switch the channel to a different zone site
Reduce interference
  Low power transmitters are employed

## Slide 22: The Switching System (SS):
Performs call processing and subscriber-related functions
The system includes the following functional units:
  Mobile Services Switching Center (MSC)
  Home Location Register (HLR)
  Visitor Location Register (VLR)
  Authentication Center (AUC)
  Equipment Identity Register (EIR)

## Slide 23: Mobile Services Switching Center (MSC)
The main element within the core network area of the overall GSM network architecture is the Mobile switching Services Centre (MSC).
It include registration, authentication, call location, inter-MSC handovers and call routing to a mobile subscriber.
It also provides an interface to the PSTN so that calls can be routed from the mobile network to a phone connected to a landline.

## Slide 24: Home Location Register (HLR):
The HLR is the most important database
  Storage and management of subscriptions
  Permanent data includes
    Subscriber’s service profile
    Subscriber’s location information
    Subscriber’s activity status
  In this way, the GSM network is able to route calls to the relevant base station for the MS.
  When a user switches on their phone, the phone registers with the network and from this it is possible to determine which BTS it communicates with.

## Slide 25: Visitor Location Register (VLR):
The VLR contains temporary data about visiting (roaming) subscribers
  It’s always integrated with the MSC
  When a roamer enters the service area the VLR queries the appropriate HLR
  If a roamer makes a call the VLR will already have the information it needs for call setup

## Slide 26: Authentication Center (AuC):
The AuC verifies the identity of the user and ensures the confidentiality of each call
  By providing authentication and encryption parameters for each call
  Protects network operators from fraud
  Assures a certain level of security for the content of each call

## Slide 27: Equipment Identity Register (EIR):
The EIR is a database that includes info solely about the identity of mobile equipment
  he EIR is the entity that decides whether a given mobile equipment may be allowed onto the network.
  International Mobile Equipment Identity (IMEI) number prevents calls from stolen, unauthorized, or defective mobile stations
  The AUC and the EIR can be implemented as stand-alone nodes or as a combined AUC/EIR node

## Slide 28: The Base Station System (BSS)
The Base Station Subsystem (BSS) section of the GSM network architecture that is fundamentally associated with communicating with the mobiles on the network. It consists of two elements:
The Base Transceiver Station (BTS)
  The Base Station Controller (BSC)

## Slide 29: The Base Station System (BSS):
The Base Transceiver Station (BTS)
  The BTS is the defining element for each cell.
  Handles the radio interface to the mobile unit
  Consists of tranceivers and cell antennas
  A group of BTSs is controlled by a BSC

## Slide 30: The Base Station System (BSS):
  The Base Station Controller (BSC)
  It controls a group of BTSs, and is often co-located with one of the BTSs in its group.
  It manages the radio resources and controls items such as handover within the group of BTSs, allocates channels.
  Provides all control functions and physical links between the MSC and the BTS
  A group of BSCs is served by an MSC

## Slide 31: Operation and Support Center (OSS):
  It is used to control and monitor the overall GSM network and it is also used to control the traffic load of the BSS.
  It is connected with all the equipment in the switching center and to the BSC
  Provides centralized cost-effective support
  Provides a network overview at any moment
  Supports maintenance and operational activities for different organizations and groups

## Slide 32
Thank You !!!
Any Questions ???